## Slide 1: Aerodynamics in F1 and formula student
Jonas Pangerl
Aerodynamicist
Williams Racing

## Slide 2: CONTENTS
FUNDAMENTALS
FORMULA 1 AERODYNAMIC DEVELOPMENT
UNDERSTANDING DEVELOPMENT METRICS
HOW TO IMPROVE YOUR DEVELOPMENT PROCESS
COMMON FORMULA STUDENT MISTAKES

## Slide 3: About me
University: UAS Esslingen
Formula Student (Sub-team Aerodynamics and CFD) from 2017-2021
Master Thesis at Williams Racing about high fidelity CFD simulations
Engineering Design Judge at FS East 2022
Aerodynamicist at Williams Racing

## Slide 4: Fundamentals

## Slide 5: Laptime improvements through Aerodynamics
Schuetz, Thomas. (2016). Aerodynamics of Road Vehicles (5th Edition)
Katz, Joseph. (1995). Race Car Aerodynamics: Designing for Speed

## Slide 6: Aerodynamic coefficients
Why coefficients?
Normalization of variables
Compare different driving speeds
Compare different dimensions of the car (WT and full size)
  Lift: CL
  Drag: CD
  Static pressure: Cp
  Total pressure (energy): total Cp  CpT

## Slide 7: Aerodynamic Testing Restrictions in F1
Defined in the FIA Formula 1 Sporting Regulations
Goal: limit development time, balance performance between teams, limit costs
CFD
  RATG: restricted aerodynamic test geometry  limits number of different geometries to be simulated
  MAUh: Mega Allocation Unit hours  limits solving effort over all RATGs
Wind tunnel
  Runs  limits number of wind tunnel runs
  Wind On Time  limits time where tunnel airspeed is above 5 m/s
  Occupancy  limits working time in/around the tunnel
Track
  Testing to take place only in official Free Practice sessions
FIA 2022 Formula 1 Sporting Regulations
Requires high efficient simulations

## Slide 8: Formula 1 aerodynamic development

## Slide 9: Development path
Regulations
Idea generation
CFD development
Wind tunnel testing
Track testing
Aero testing restrictions (ATR)

## Slide 10: Idea Generation
Flow field targets
Onset CpT and wake management
Yaw and ride height characteristics
Cooling performance
Load distribution
Geometry comes from aero perspective

## Slide 11: CFD
CFD is first design tool
Allows a deep insight in flow field
Quick turnaround times
Balancing between accuracy and efficiency (RANS, DES, …)
Automated investigation available (Adjoint solver, …)
Run limited number of conditions
 Be aware of limitations!

## Slide 12: Transient CFD
Resolves transient effects
More accurate but computationally expensive
Understand where it is needed and how you can use the data
Wall resolved Large-Eddy-Simulation

## Slide 13: Wind Tunnel Testing
Physical aerodynamics testing at scale
External aerodynamics modelling
Regulated by ATR
Develop a stable and predictable car
Fewer options for detailed analysis
Compromised cornering simulation compared to CFD and track

## Slide 14: Wind tunnel testing
Off-surface flow field data:
Particle Image Velocitimetry (PIV)
Rakes
Kiel probes

## Slide 15: Wind tunnel testing
Off-surface flow field data:
Particle Image Velocitimetry (PIV)
Rakes
Kiel probes
On-surface flow field data:
Pressure tappings
Flow Viz
Wool Tufts

## Slide 16: Wind Tunnel Testing
Develop a stable and predictable car:
Smooth sweeps, remove peaks
Performance where you want to set-up the car (high rake vs low rake)
Understand where structures break down, flow separates, …
BASELINE
OPTION

## Slide 17: Wind Tunnel Testing
Develop a stable and predictable car:
Smooth sweeps, remove peaks
Performance where you want to set-up the car (high rake vs low rake)
Understand where structures break down, flow separates, …
BASELINE
OPTION

## Slide 18: Wind Tunnel Testing
Develop a stable and predictable car:
Smooth sweeps, remove peaks
Performance where you want to set-up the car (high rake vs low rake)
Understand where structures break down, flow separates, …
BASELINE
OPTION

## Slide 19: Track Testing
Real world testing
Driver feedback
Unstable and noisy conditions
Less data
Limited time

## Slide 20: Understanding development metrics

## Slide 21: Front wing Polar
Total DF
AeroBal
Mid FWF
High FWF
FWDs AB
RWDs AB
Low FWF
Front Wing Flap (FWF) to adjust aerodynamic balance between front and rear axle

## Slide 22: Front wing Polar
Front Wing Flap (FWF) to adjust aerodynamic balance between front and rear axle
Development options need to be „above“ polar to improve overall performance
Otherwise we could just crank up the FWF to get the same aero balance and also more downforce
Consider new behaviour over FWF angles
Total DF
AeroBal
Mid FWF
High FWF
FWDs AB
RWDs AB
Dev 2
Dev 1
Low FWF
Dev 2
Dev 1
“above polar”
“below polar”

## Slide 23: Front wing Polar
Total DF
AeroBal
Mid FWF
High FWF
FWDs AB
RWDs AB
Low FWF
Dev 3
“above polar”
“below polar”

## Slide 24: Rear Wing Polar
Different rear wings to select the right drag level for the given circuit
Development options (not only rear wings) need to beat polar to provide an overall benefit
Total DF
Drag
Low DF
(Gurney)
Mid DF
(Gurney)
High DF
(Gurney)
Dev 1
Dev 2

## Slide 25: Rebalancing and Redragging
Balance and aerodynamic efficiency must be considered in development
Approximate linear downforce/balance ratio from FW polar
Approximate linear downforce/drag ratio from RW polar
Calculate „headline“ number with total downforce and ratios to get an overall number that indicates the performance benefit

## Slide 26: How to improve your development process

## Slide 27: IDEA & Concept generation
Statement: “Most Formula Student cars lack a comprehensive flow field concept.”
Analyse your current concept:
  Where could I improve onset CpT

## Slide 28: IDEA & Concept generation
Statement: “Most Formula Student cars lack a comprehensive flow field concept.”
Analyse your current concept:
  Where could I improve onset CpT
  How is the wheel wake management

## Slide 29: IDEA & Concept generation
Statement: “Most Formula Student cars lack a comprehensive flow field concept.”
Analyse your current concept:
  Where could I improve onset CpT
  How is the wheel wake management
  Where do I need more “fresh” air

## Slide 30: IDEA & Concept generation
Statement: “Most Formula Student cars lack a comprehensive flow field concept.”
Analyse your current concept:
  Where could I improve onset CpT
  How is the wheel wake management
  Where do I need more “fresh” air
  What happens in cornering/under yaw or at extreme ride heights
  How could I improve my radiator performance
  Where do I want to put my wasted air
  Where could I have instabilities (vortex brake down, separation, …)
  How could I improve the interaction between different components

## Slide 31: IDEA & Concept generation
Statement: “Most Formula Student cars lack a comprehensive flow field concept.”
Analyse your current concept:
  Where could I improve onset CpT
  How is the wheel wake management
  Where do I need more “fresh” air
  What happens in cornering/under yaw or at extreme ride heights
  How could I improve my radiator performance
  Where do I want to put my wasted air
  Where could I have instabilities (vortex brake down, separation, …)
  How could I improve the interaction between different components
Decide on your flow field objectives
NOT: where could I put a wing to see what it does!

## Slide 32: IDEA & Concept generation
Statement: “Most Formula Student cars lack a comprehensive flow field concept.”
Analyse your current concept:
  Where could I improve onset CpT
  How is the wheel wake management
  Where do I need more “fresh” air
  What happens in cornering/under yaw or at extreme ride heights
  How could I improve my radiator performance
  Where do I want to put my wasted air
  Where could I have instabilities (vortex brake down, separation, …)
  How could I improve the interaction between different components
Decide on your flow field objectives
Develop towards your target, do not focus on numbers at the beginning
Try different concepts, do not waste time with too much detailing
Decide for a concept and refine it

## Slide 33: IDEA & Concept generation - EXAMPLE
old wing
new wing
Example Rennstall Front Wing development
Flow field objectives:
Improve onset CpT to rear
More continuous behaviour through yaw and ride height
More downforce
Adjustable aero balance

## Slide 34: IDEA & Concept generation - EXAMPLE
new FW
old FW
Chart: AVG TOTAL CpT
| 70 | 60 | 50 | 40 | 30 | 20
neuer FW | 0.782 | 0.74295 | 0.73255 | 0.53706 | 0.52951 | 0.48627
alter FW | 0.59788 | 0.53848 | 0.48499 | 0.42533 | 0.37809 | 0.32506
old wing
new wing

## Slide 35: IDEA & Concept generation - EXAMPLE
leeward
windward
new FW
old FW
y=0

## Slide 36: CAD and Airfoils

## Slide 37: CAD
Create your own airfoils, do not use predefined ones

## Slide 38: CAD
Create your own airfoils, do not use predefined ones
make the airfoils adjustable:
  Onset angle
  LE thickness
  Curvature distribution
  Departure angle
Keep an eye on curvature

## Slide 39: CAD
Create your own airfoils, do not use predefined ones
make the airfoils adjustable:
  Onset angle
  LE thickness
  Curvature distribution
  Departure angle
Keep an eye on curvature
Avoid sharp angles and transitions  use blends and fillets
Keep shedding edges sharp

## Slide 40: Airfoils
Onset Flow
Stagnation point on leading edge
Highest curvature on stagnation point
Curvature continuity between pressure and suction side
Increase leading edge radius (decrease curvature) in case of variable onset angles

## Slide 41: Airfoils
Onset Flow
Stagnation point on leading edge
Highest curvature on stagnation point
Curvature continuity between pressure and suction side
Increase leading edge radius (decrease curvature) in case of variable onset angles

## Slide 42: Airfoils
Departing Flow
Increase departure angle for higher load
Decrease angle to keep flow attached

## Slide 43: Airfoils
Curvature distribution
Defines pressure distribution
  Cp peak
  Adverse pressure gradient (length & gradient of Cp recovery)
  Drag and thrust components
Move curvature forwards to
  Support upstream profiles
  Reduce drag
  Increase recovery length and gradient
  Force transition
Laminar separation bubble
Re-attachement point
Suction peak
Pressure recovery region
Cp

## Slide 44: Airfoils
Curvature distribution
Defines pressure distribution
  Cp peak
  Adverse pressure gradient (length & gradient of Cp recovery)
  Drag and thrust components
Move curvature forwards to
  Support upstream profiles
  Reduce drag
  Increase recovery length and gradient
  Force transition
Equally distribute curvature to
  Reduce boundary layer growth
  Create maximum load
  needs support from downstream geometry
Pressure recovery region
Cp

## Slide 45: Multi Element Wing Cascades
Why more elements?
Re-energize boundary layer on suction surface
Increase capability of flow turning
DRS implementation (rear wing)
Delay/avoid stall at low ride heights (front wing)
Why less elements?
More load
Less lossy departing flow
Easier to develop
Lighter

## Slide 46: Multi Element Wing Cascades
Slot gaps
Allow high energy flow from pressure side to suction side
Decrease slot gap size to
  Support upstream profile
  Increase overall load
Increase slot gap size to
  Allow more air going through
  Support downstream profile

## Slide 47: Multi Element Wing Cascades
Curvature
Avoid large Cp jumps between elements
Move curvature forward to support upstream element
Supported elements can have significant amount of trailing edge curvature

## Slide 48: Multi Element Wing Cascades
Departure angle
Leave space for flow through slot gap
Increase departure angle to transfer load to forward element (offload upstream element)
Decrease departure angle to transfer load to downstream element

## Slide 49: Multi Element Wing Cascades
Departure angle
Leave space for flow through slot gap
Increase departure angle to transfer load to forward element (offload upstream element)
Decrease departure angle to transfer load to downstream element

## Slide 50: Multi Element Wing Cascades
Departure angle
Leave space for flow through slot gap
Increase departure angle to transfer load to forward element (offload upstream element)
Decrease departure angle to transfer load to downstream element

## Slide 51: Muti Element Wing Cascades

## Slide 52: Optimizing the CFD Process
Chart: Improvement in Lap Time (s)
| Event 1 | Event 2 | Event 3 | Event 4 | Event 5 | Event 6 | Event 7 | Event 8 | Event 9 | Event 10 | Event 11 | Event 12 | Event 13 | Event 14 | Event 15 | Event 16 | Event 17 | Average
Typical Development Rate | 0 | 0.1 | 0.18 | 0.25 | 0.65 | 0.7 | 0.7 | 0.78489 | 1 | 1.12 | 1.15 | 1.3 | 1.4 | 1.4 | 1.55 | 1.75 | 1.8

## Slide 53: Optimizing the CFD Process
Chart: Improvement in Lap Time (s)
| Event 1 | Event 2 | Event 3 | Event 4 | Event 5 | Event 6 | Event 7 | Event 8 | Event 9 | Event 10 | Event 11 | Event 12 | Event 13 | Event 14 | Event 15 | Event 16 | Event 17 | Average
Typical Development Rate | 0 | 0.1 | 0.18 | 0.25 | 0.65 | 0.7 | 0.7 | 0.78489 | 1 | 1.12 | 1.15 | 1.3 | 1.4 | 1.4 | 1.55 | 1.75 | 1.8
Increased Development Rate | 0 | 0.15 | 0.27 | 0.375 | 0.975 | 1.05 | 1.05 | 1.1773 | 1.5 | 1.68 | 1.725 | 1.95 | 2.1 | 2.1 | 2.325 | 2.625 | 2.7
Improving the Tool Kit
Improved simulation accuracy
Better utilisation of data
Quicker turnaround times

## Slide 54: Optimizing the CFD Process
Chart: year
| 2012 | 2013 | 2014 | 2015 | 2016 | 2017 | 2018 | 2019 | 2020 | 2021
# cells | 10 | 10 | 12 | 24 | 32 | 36 | 44 | 110 | 90 | 90
smarter mesh
improve accuracy
new cluster

## Slide 55: Optimizing the CFD Process
Chart: year
| 2012 | 2013 | 2014 | 2015 | 2016 | 2017 | 2018 | 2019 | 2020 | 2021
# cells | 10 | 10 | 12 | 24 | 32 | 36 | 44 | 110 | 90 | 90
equivalent # cells | 10 | 10 | 12 | 24 | 32 | 36 | 44 | 110 | 135 | 135
Changed spatial resolution of vol. mesh

## Slide 56: Optimizing the CFD Process
Chart: year
| 2012 | 2013 | 2014 | 2015 | 2016 | 2017 | 2018 | 2019 | 2020 | 2021
CAD2CFD | 0.16667 | 0.16667 | 0.16667 | 0.16667 | 0.16667 | 0.16667 | 0.16667 | 0.25 | 0.016667 | 0.016667
# cells | 10 | 10 | 12 | 24 | 32 | 36 | 44 | 110 | 90 | 90
equivalent # cells | 10 | 10 | 12 | 24 | 32 | 36 | 44 | 110 | 135 | 135
Fully automated CAD import

## Slide 57: Optimizing the CFD Process
Chart: year
| 2012 | 2013 | 2014 | 2015 | 2016 | 2017 | 2018 | 2019 | 2020 | 2021
CAD2CFD | 0.16667 | 0.16667 | 0.16667 | 0.16667 | 0.16667 | 0.16667 | 0.16667 | 0.25 | 0.016667 | 0.016667
meshing | 0.33333 | 0.33333 | 0.41667 | 0.58333 | 0.66667 | 0.75 | 0.83333 | 1.1667 | 0.33333 | 0.33333
# cells | 10 | 10 | 12 | 24 | 32 | 36 | 44 | 110 | 90 | 90
equivalent # cells | 10 | 10 | 12 | 24 | 32 | 36 | 44 | 110 | 135 | 135
Improved surface meshing

## Slide 58: Optimizing the CFD Process
Chart: year
| 2012 | 2013 | 2014 | 2015 | 2016 | 2017 | 2018 | 2019 | 2020 | 2021
CAD2CFD | 0.16667 | 0.16667 | 0.16667 | 0.16667 | 0.16667 | 0.16667 | 0.16667 | 0.25 | 0.016667 | 0.016667
meshing | 0.33333 | 0.33333 | 0.41667 | 0.58333 | 0.66667 | 0.75 | 0.83333 | 1.1667 | 0.33333 | 0.33333
solving | 2 | 2 | 2.0833 | 4.1667 | 4.6667 | 5 | 6.3333 | 8 | 6.6667 | 3.6667
# cells | 10 | 10 | 12 | 24 | 32 | 36 | 44 | 110 | 90 | 90
equivalent # cells | 10 | 10 | 12 | 24 | 32 | 36 | 44 | 110 | 135 | 135
Initialization with old solution
Improved solver settings
Converged in less than 700 iterations
Auto convergence detection

## Slide 59: Optimizing the CFD Process
Chart: year
| 2012 | 2013 | 2014 | 2015 | 2016 | 2017 | 2018 | 2019 | 2020 | 2021
CAD2CFD | 0.16667 | 0.16667 | 0.16667 | 0.16667 | 0.16667 | 0.16667 | 0.16667 | 0.25 | 0.016667 | 0.016667
meshing | 0.33333 | 0.33333 | 0.41667 | 0.58333 | 0.66667 | 0.75 | 0.83333 | 1.1667 | 0.33333 | 0.33333
solving | 2 | 2 | 2.0833 | 4.1667 | 4.6667 | 5 | 6.3333 | 8 | 6.6667 | 3.6667
posting | 0.33333 | 0.33333 | 0.33333 | 0.5 | 0.5 | 0.58333 | 1 | 1.75 | 0.13333 | 0.13333
# cells | 10 | 10 | 12 | 24 | 32 | 36 | 44 | 110 | 90 | 90
equivalent # cells | 10 | 10 | 12 | 24 | 32 | 36 | 44 | 110 | 135 | 135
new posting software

## Slide 60: Optimizing the CFD Process
Improving the Tool Kit
Focus on where you can improve the most
Invest time & assign members to the process
Make things easy for future generations
Chart: year
| 2012 | 2013 | 2014 | 2015 | 2016 | 2017 | 2018 | 2019 | 2020 | 2021
CAD2CFD | 0.16667 | 0.16667 | 0.16667 | 0.16667 | 0.16667 | 0.16667 | 0.16667 | 0.25 | 0.016667 | 0.016667
meshing | 0.33333 | 0.33333 | 0.41667 | 0.58333 | 0.66667 | 0.75 | 0.83333 | 1.1667 | 0.33333 | 0.33333
solving | 2 | 2 | 2.0833 | 4.1667 | 4.6667 | 5 | 6.3333 | 8 | 6.6667 | 3.6667
posting | 0.33333 | 0.33333 | 0.33333 | 0.5 | 0.5 | 0.58333 | 1 | 1.75 | 0.13333 | 0.13333
# cells | 10 | 10 | 12 | 24 | 32 | 36 | 44 | 110 | 90 | 90
equivalent # cells | 10 | 10 | 12 | 24 | 32 | 36 | 44 | 110 | 135 | 135

## Slide 61: Optimizing THE CFD visualization
Report the simulations and compare them
Use simple techniques to allow a first conclusion

## Slide 62: Optimizing THE CFD visualization
Report the simulations and compare them
Use simple techniques to allow a first conclusion
Use delta plots to highlight flow field and pressure deltas
Slice geometry and plot Cp distribution

## Slide 63: Optimizing THE CFD visualization
Off-surface data:
Focus on energy content of air (total pressure  CpT)
Use mainly x-slices to understand the flow field
Additionally use static pressure (Cp) and vortex visualization (vorticity, Q-criterion, Lambda2-criterion, Rotex, …)
Velocity vectors
Surface data:
Static pressure
Streamlines
Wall shear stress

## Slide 64: TESTING & VALIDATION
Wool Tufts
Flow Vis paint
Spring travel  downforce
Coasting test  drag
Pressure Tapping
Rake
Greenteam Uni Stuttgart

## Slide 65: TESTING & VALIDATION
old FW
new FW
40 mm RH
30 mm RH
Front wing pressure tappings in straight line
Chart: Ride Height (mm)
| 70 | 60 | 50 | 40 | 30 | 20
neuer FW | 1.7103 | 1.8145 | 1.8851 | 1.9739 | 2.1383 | 2.3457
alter FW | 1.5941 | 1.6518 | 1.7067 | 1.7522 | 1.7822 | 1.8332

## Slide 66: Common Formula Student mistakes

## Slide 67: Common Formula Student mistakes
CFD
High wall y+ for the whole car
  Use high Reynolds approach where you don’t need to fully resolve the boundary layers
  Low Reynolds approach only where you really need it (suction surfaces of wings etc.)
low quality CFD simulations (< 20 mio cells for fullcar simulation)
  Be aware of possible issues, do not assume you get the right solution
  Perform a mesh study
  Compare your results with a better resolved flow field
  Only refine where it is really necessary
  Can you use different mesh settings for developing different areas on the car?
2D simulations
  A race car is 3D!
  You can not even develop a front wing profile in clean flow in 2D
  You can use 2D to understand fundamentals of airfoils etc. but not to develop components for your car
Transient simulations (RANS)
  Focus on improving your steady-state simulation first
  Transient simulations should use at least DES approach
  Use a finer mesh for DES. This still does not give you the real flow field

## Slide 68: Common Formula Student mistakes
CFD
Validate the simulations
  Use at least wool tufts to make sure your wings don’t separate
  Wool tufts and flow viz on pressure sides is useless
  Validation is not something you only do for the engineering design event
Make the most out of your CFD results
  Use the right flow variables for the visualization
  Are y-sections always the best?
Total Cp
Velocity
Cp

## Slide 69: Common Formula Student mistakes
Aero concept
Define your design goals appropriately
  Lift/drag target
  Aero balance target
  Use lap time simulations or experience from previous years
  How much do you benefit from your aero?
  Do not copy from F1
Do not design the car for straight ahead only
  imagine what will happen under yaw if you can not run cornering or yaw simulations
  Use wing profiles at leading edges of endplates
Use the right wing profiles
  (high lift) airfoils from a online database are not designed for running in a multi element config or in close proximity to the ground
Design your wing cascades properly
  Make sure there is a good reason to use more than one element
  Pay attention to the slot gaps. While designing them but also in manufacturing
Integrate cooling into the aero package
  It is not something for the powertrain or battery guys
  Optimize your onset flow and manage the departing flow

## Slide 70: Thank you!